## Slide 1: LC-3 Assembly Language

## Slide 2: Programming
Machine Language (object code) – The series of binary numbers that the computer can understand directly. May or may not be ready to run for various reasons.
Assembly Language - A human readable (sort of) way to write code that the computer can easily turn into machine language.
High Level Language – A MORE human readable (sort of) way to write assembly language.
  GCC converts C and C++ to assembly then to object code.
  Java does something a little different (bytecode and JRE)
Executable Image – The machine language program AFTER it has been finished and is ready to run on the processor.

## Slide 3: Instructions
An instruction has two parts:
  opcode : The operation being performed.
    These are divided into three categories: Operate, Data Movement, and Control
    LC3 has 15 opcodes (ADD, AND, BR, JMP, JSR, JSRR, LD, LDI, LDR, LEA, NOT, RET, RTI, ST, STI, STR, TRAP)
  operands : The data to use in the operation.
    This data is read from somewhere as specified by the instruction and the addressing mode
    LC3 has 5 addressing modes (Immediate, Register, PC-Relative, Indirect, Base+Offset)

## Slide 4
See appendix A

## Slide 5: Opcode Summary
Add - ADD value in a register to a value in a register. Store result in a register.
Add - ADD value in a register to a number. Store result in a register.
And - Bitwise AND value in a register to a value in a register. Store result in a register. (The term BITWISE is explained when we discuss AND.)
And - Bitwise AND value in a register to a number. Store result in a register.
Not – Invert all of the bits in a register and store the result in a register.
BR, BRNZP – Conditional branch. Like if statement.
LD, LDR, LDI – Load register with a value from memory
ST, STR, STI – Store register value somewhere in memory.
LEA – Load an address into a register and not the data.
JMP – Jump execution to some other place in memory.
JSR, JSRR – Jump to a subroutine similar to a function or method.
RET – Return from the subroutine
RTI – Return from interrupt, restores process information.
TRAP – System call. Like an operating system. Handles input and output.

## Slide 6: Simple Example Program
Labels | Opcode | Operands | Comment | Hex Value
 | .orig | X3000 | ;Specify starting memory | 3000
 | GETC |  | ;R0 <- Keyboard character | F020
 | LD | R3, #9 | ;R3 <- -48 | 2609
 | ADD | R1, R0, R3 | ;R1 <- R0 + R3 | 1203
 | GETC |  | ;R0 <- Keyboard character | F020
 | ADD | R2, R0, R3 | ;R2 <- R0 + R3 | 1403
 | ADD | R0, R1, R2 | ; R0 <- R1 + R2 | 1042
 | NOT | R3, R3 | ; R3 <- ~R3 | 96FF
 | ADD | R3, R3, #1 | ;R3 <- R3 + 1 | 16E1
 | ADD | R0, R0, R3 | ;R0 <- R0 + R3 | 1003
 | OUT |  | ;Display <- R0 | F021
 | HALT |  | ;End of program | F025
 | .fill -48 |  |  | FFD0
 | .end |  | ;End of file | 

## Slide 7: Running a program
Program is loaded into memory at x3000
Program Counter (PC) is set to x3000
The instruction pointed to by the PC is loaded into the Instruction Register (IR).
The PC is incremented at the same time as the loading of the IR.
The instruction is processed and executed.
Repeat until halt is reached.
Note that some instructions change the PC which causes branching.

## Slide 8: Data Types and Condition Codes
An ISA can have different data types.
  LC3 uses 2's complement numbers (Review of 2s complement below.)
Condition codes are special flags that get set when certain operations occur.
  LC3 uses N, P, and Z
    N – is set if the result of an operation is negative.
    P – is set if the result of an operation is positive (redundant?).
    Z – is set if the result of an operation is zero.
  Other common flags (that are not in the LC3)
    C – the result of the carry out of an add operation
    v – set in the even of an overflow condition

## Slide 9: Registers
Eight general purpose registers (R0 – R7).
Instruction Register (IR)– Holds the instruction in the microprocessor so it can be interpreted.
Program Counter (PC) – Holds the address of the next program step. Looping is accomplished by changing the value of the PC.
Memory Address Register (MAR) – When transferring to/from memory, this will hold the address of the memory unit to be written or read.
Memory Data Register (MDR) – When transferring to memory, this holds the value to save. When transferring from memory, this holds the value read.
KeyBoard Data Register (KBDR) – Holds the ASCII character of the key after it has been typed.
KeyBoard Status Register (KBSR) – Status information that lets the microprocessor know a key has been typed and is ready to be read.
Display Data Register (DDR) – Holds the ASCII character to display on the screen.
Display Status Register (DSR) – Status information. Use this to tell the display you are ready to write the character from the DDR to the screen.
Process State Register (PSR) – Information about the current state of the current program.

## Slide 10: Operate Instructions
On LC3 all operate instructions use register or immediate addressing mode.
15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
Add |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | DR |  |  | SR1 |  |  | 0 | 0 | 0 | SR2 |  | 
0 | 0 | 0 | 1 | DR |  |  | SR1 |  |  | 1 | Immediate |  |  |  | 
And |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 1 | DR |  |  | SR1 |  |  | 0 | 0 | 0 | SR2 |  | 
0 | 1 | 0 | 1 | DR |  |  | SR1 |  |  | 1 | Immediate |  |  |  | 
Not |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 | 0 | 0 | 1 | DR |  |  | SR |  |  | 1 | 1 | 1 | 1 | 1 | 1
Notes: Describe ADD here

## Slide 11: Operate Instructions
On LC3 all operate instructions use register or immediate addressing mode.
15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
Add |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | DR |  |  | SR1 |  |  | 0 | 0 | 0 | SR2 |  | 
0 | 0 | 0 | 1 | DR |  |  | SR1 |  |  | 1 | Immediate |  |  |  | 
And |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 1 | DR |  |  | SR1 |  |  | 0 | 0 | 0 | SR2 |  | 
0 | 1 | 0 | 1 | DR |  |  | SR1 |  |  | 1 | Immediate |  |  |  | 
Not |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 | 0 | 0 | 1 | DR |  |  | SR |  |  | 1 | 1 | 1 | 1 | 1 | 1

## Slide 12: Bitwise
AND & NOT are bitwise operations
Bitwise means it applies the operations you expect but applies the operation on each bit of a binary number.
Bitwise operators ARE NOT logical. They DO NOT use Boolean argument.
Bitwise AND uses single ampersand (&)
Bitwise NOT uses the tilde (~)

## Slide 13: AND Example
Assume four bit unsigned numbers.
Each pair of bits from the two different values have the AND operator applied.
For bitwise operations, 1 is true and 0 is false.
And means they both have to be true for the output to be true
1001 0011
&1100 &0101

## Slide 14: AND Example
Assume four-bit unsigned numbers
Each pair of bits from the two different values have the AND operator applied.
For bitwise operations 1 is true and 0 is false.
And means they both have to be true for the result to be true
1001 (9) 0101 (5)
&1100 (12) &0011 (3)
1000 (8) 0001 (1)
Try it in java:
System.out.println(9 & 12);
System.out.println(5 & 1);

## Slide 15: NOT Example
NOT is a complement. ALL bits are inverted.
Assuming 4-bit unsigned numbers.
~1001 (~9) becomes 0110 (6)
What about Java? What would the following print?
System.out.println(~9);

## Slide 17: Operate Instructions
With only ADD, AND, NOT…
  R1 = 5, R2 = 3, R3 = 0
  Perform the following (write the code in hex)
  R1 <- R2 – R1 (Subtraction)
  R1 <- R2 | R1 (Bitwise or)
  R1 <- R2 (Transfer)
  R1 <- 0 (Clear)

## Slide 18: Data Movement Instructions
Moving data from
  Register to memory
  Memory to register
  (Register to register is covered under operate instructions)
Addressing modes
  Immediate
  PC-Relative
  Indirect
  Base + offset

## Slide 19: 2's Complement
Allows both positive and negative numbers
Works because of a fixed number of bits
Assume you have only 5 bits to work with
You can store 00000 to 11111
Adding a number to its additive identity should give zero so 7 + (-7) = 0
00111 (7)
+11001 (?)
00000 (0)
11001 must be -7

## Slide 20: Decimal to 2's Complement
If the number is positive
  Treat as unsigned binary
If the number is negative
  Convert as unsigned
  Invert all bits and add 1
Convert 17 and -23 to 6 bit 2's complement

## Slide 21: Decimal to 2's Complement Example
Convert 17 and -23 to 6 bit 2's complement
  17 (Positive so treat as unsigned binary and done)
  17 = 16 + 1 = 010001 (make sure to write the number as six bits)
  Answer: 010001
  -23 (negative so convert as unsigned then do the following)
  23 = 16 + 4 + 2 + 1 = 010111 (six bits is important)
  101000 (invert all bits)
  101001 (add 1)
  Answer: 101001 (How can you verify this is -23?)

## Slide 22: PC Relative
Uses the current value of the program counter
Adds a value specified in the instruction.
  LD – Load value from memory and place it into a register.
  ST – Stores register value in memory.
4 bit opcode, 3 bit register, 9 bit value
Value is 9 bit 2's compliment (Range?)
Effective address – The ACTUAL address of the operand. This is the value after all calculations and redirections have been made.

## Slide 23: PC Relative
LD – Load value from memory and place it into a register.
ST – Save value from register to memory
Load what is stored in memory location PC + x0AF into R2
Assume this LD is stored at x3000, what is the effective address?
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
LD |  |  |  | R2 |  |  | x0AF |  |  |  |  |  |  |  | 

## Slide 24: PC Relative
LD – Load value from memory and place it into a register.
Assume this LD is stored at x3000, what is the effective address? x30B0
Remember the PC is incremented after loading the instruction.
Assume x0035 is stored at memory location x30B0
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | Address Gen Bits |  |  |  |  |  |  |  | 
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
LD |  |  |  | R2 |  |  | x0AF |  |  |  |  |  |  |  | 

## Slide 25: Example: Add 3 Numbers
Add three numbers.
  Start program at x3000
  Values 5,7,and 17 are stored at locations x3080, x3081, and x3082.
  The sum will be stored in x3083
  Only use PC-Relative addressing
    LD (0010)
    ST (0011)
  Will also need add (0001) (Which add?)

## Slide 26: Formats
How can we add three numbers stored in memory?
How many registers will we need? Minimize this as much as possible.
I recommend zeroing registers before use.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
LD (0010) |  |  |  | DR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
ST (0011) |  |  |  | SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
Add (0001) |  |  |  | DR |  |  | SR1 |  |  | 0 | 0 | 0 | SR2 |  | 
And(0101) |  |  |  | DR |  |  | SR |  |  | 1 | 2's comp value |  |  |  | 

## Slide 27
R0 |  |  | 3080 | 5 |  |  | 
R1 |  |  | 3081 | 8 |  |  | 
R2 |  |  | 3082 | 11 |  |  | 
R3 |  |  | 3083 | ? |  |  | 
R4 |  |  |  |  |  |  | 
R5 |  |  |  |  |  |  | 
R6 |  |  |  |  |  |  | 
R7 |  |  |  |  |  |  | 
How could we get the sum of these three numbers stored
in memory location x3083?
You can only do one of the following:
-Move memory to register
-Move register to memory
-Add two registers and store in a register

## Slide 28
R0 |  |  | 3000 |  |  | 3080 | 5
R1 |  |  | 3001 |  |  | 3081 | 8
R2 |  |  | 3002 |  |  | 3082 | 11
R3 |  |  | 3003 |  |  | 3083 | ?
R4 |  |  | 3004 |  |  |  | 
R5 |  |  | 3005 |  |  |  | 
R6 |  |  | 3006 |  |  |  | 
R7 |  |  | 3007 |  |  |  | 
 |  |  | 3008 |  |  |  | 
Clear R0
Load R1 with first number.
Add R0 to R1 and store in R0
Load R1 with second number.
Add R0 to R1 and store in R0
Load R1 with third number.
Add R0 to R1 and store in R0
Store R0 to memory.

## Slide 29: Homework 1 & 2
USE THE DOCUMENTS ON ASULEARN FOR DETAILS ABOUT THESE ASSIGNEMNTS
Homework 1
  Add three numbers.
  The first homework is to get the previous problem working in the LC3.
Homework 2
  Modify the previous assignment
  Add 4 numbers and subtract a 5th.

## Slide 30: Indirect Addressing
LDI – Load Indirect – Memory to Register
STI – Store Indirect – Register to Memory
  LDI and STI are very similar to LD and ST.
  Memory calculation for operand is that same, however, the address calculated is NOT actually the operand.
  The address calculated is the address of the operand. (TRICKY)
  Indirect has one extra step and needs an extra memory access to get the operand.

## Slide 31: Load Indirect
LDI – Load value from memory and use it as the address of the actual data to move into a register.
MAR <- PC + x1AF
MDR <- MEM[MAR]
MAR <- MDR
R2 <- MEM[MAR]
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
LDI |  |  |  | R2 |  |  | x1AF |  |  |  |  |  |  |  | 

## Slide 32: Store Indirect
STI – Save value from register to address specified in memory location.
MAR <- PC + x1AF
MAR <- MEM[MAR] (Can this be done in one cycle?)
MDR <- MEM[MAR]
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
STI |  |  |  | R2 |  |  | x1AF |  |  |  |  |  |  |  | 

## Slide 33
Address | Value | 
3000 | A403 | LDI R2, #3 (1010 0100 0000 0011)
3001 | 14A1 | The address is PC + 3 = 3001 + 3 = 3004
3002 | B402 | What is in address 3004?
3003 | FF25 | 
3004 | 300A | 
3005 | 300C | 
3006 | 001A | 
3007 | 00B2 | 
3008 | C133 | 
3009 | 2F25 | 
300A | 0005 | 
300B | 11E2 | 
300C | 0200 | 

## Slide 34
Address | Value | 
3000 | A403 | LDI R2, #3
3001 | 14A1 | The address is PC + 3 = 3001 + 3 = 3004
3002 | B402 | What is in address 3004? 300A
3003 | FF25 | 300A is the Effective Address
3004 | 300A | The operand is stored in 300A
3005 | 300C | What is in address 300A?
3006 | 001A | 
3007 | 00B2 | 
3008 | C133 | 
3009 | 2F25 | 
300A | 0005 | 
300B | 11E2 | 
300C | 0200 | 

## Slide 35
Address | Value |  | R2 | 5
3000 | A403 | LDI R2, #3 |  | 
3001 | 14A1 | The address is PC + 3 = 3001 + 3 = 3004 |  | 
3002 | B402 | What is in address 3004? 300A |  | 
3003 | FF25 | 300A is the Effective Address. |  | 
3004 | 300A | The operand is stored in 300A. |  | 
3005 | 300C | What is in address 300A? 5 |  | 
3006 | 001A | R2 will be loaded with 5. |  | 
3007 | 00B2 |  |  | 
3008 | C133 |  |  | 
3009 | 2F25 |  |  | 
300A | 0005 |  |  | 
300B | 11E2 |  |  | 
300C | 0200 |  |  | 

## Slide 36
Address | Value |  | R2 | 6
3000 | A403 |  |  | 
3001 | 14A1 | ADD R2, R2, #1 (0001 0100 1010 0001 |  | 
3002 | B402 | R2 <- R2 + 1 |  | 
3003 | FF25 |  |  | 
3004 | 300A |  |  | 
3005 | 300C |  |  | 
3006 | 001A |  |  | 
3007 | 00B2 |  |  | 
3008 | C133 |  |  | 
3009 | 2F25 |  |  | 
300A | 0005 |  |  | 
300B | 11E2 |  |  | 
300C | 0200 |  |  | 

## Slide 37
Address | Value |  | R2 | 6
3000 | A403 |  |  | 
3001 | 14A1 |  |  | 
3002 | B402 | STI R2, #2 (1011 0100 0000 0010) |  | 
3003 | FF25 | Store R2 somewhere. |  | 
3004 | 300A | What is the address from the instruction? |  | 
3005 | 300C |  |  | 
3006 | 001A | What is the effective address? |  | 
3007 | 00B2 |  |  | 
3008 | C133 | What gets stored where? |  | 
3009 | 2F25 |  |  | 
300A | 0005 |  |  | 
300B | 11E2 |  |  | 
300C | 0200 |  |  | 

## Slide 38
Address | Value |  | R2 | 6
3000 | A403 |  |  | 
3001 | 14A1 |  |  | 
3002 | B402 | STI R2, #2 (1011 0100 0000 0010) |  | 
3003 | FF25 | Store R2 somewhere. |  | 
3004 | 300A | What is the address from the instruction? |  | 
3005 | 300C | 3003 + 2 = 3005 |  | 
3006 | 001A | What is the effective address? |  | 
3007 | 00B2 | 300C |  | 
3008 | C133 | What gets stored where? |  | 
3009 | 2F25 | MEM[300C] <- 6 |  | 
300A | 0005 |  |  | 
300B | 11E2 |  |  | 
300C | 0006 |  |  | 

## Slide 39: Base Register + Offset
Add an immediate offset to some register.
Easier to calculate for humans.
LDR and STR
Often a register will be dedicated being the memory base.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OpCode |  |  |  | DR or SR |  |  | Base R |  |  | 2's comp value |  |  |  |  | 
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
LDR |  |  |  | R2 |  |  | R6 |  |  | #13 |  |  |  |  | 

## Slide 40: LEA and Immediate Mode
Load Effective Address (LEA) – Puts an address into a register instead of data.
Immediate because it doesn't access memory.
Add 8 bit 2's complement immediate (part of the instruction) data to PC and store in register.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OpCode |  |  |  | DR |  |  | 2's comp value |  |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
LEA |  |  |  | R5 |  |  | #-2 |  |  |  |  |  |  |  | 

## Slide 41: Addressing Modes Summary
Immediate – Data in instruction.
Register – Data is in register.
PC-Relative – Add immediate value to PC to get address of data.
Indirect – PC-Relative gives address of the address of the data and NOT the data directly.
Base + offset – Immediate value is added to an address from a register.

## Slide 42: Branching
Branch (BR) – Changes execution order if conditions are met.
Detects Negative, Positive, and Zero
Works in conjunction with one of the following instructions.
    ADD, AND, NOT, LD, LDI, LDR, LEA
If one of the above instructions results in a negative, positive, or zero value being written to a register, the appropriate flag (N, P, Z) will be set.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OpCode |  |  |  | N | Z | P | 2's comp value |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
BR |  |  |  | N |  | P | #-2 |  |  |  |  |  |  |  | 

## Slide 43: What does this do?
AND R0, R0, #0 (The # lets you know it is immediate)
AND R1, R1, #0
ADD R0, R0, #6
ADD R1, R1, R0
ADD R0, R0, #-1
BRP #-3
TRAP HALT (What is stored in R1?)

## Slide 44: Looping and Branching
if (R2 > R1) {
R2 <- R2 + R1
}
We have to translate if(R2 > R1) into a BRNZP.
How? Subtraction.
In assembly language, it is easier to think of this as:
"IF THE CONDITION IS FALSE, JUMP OVER THE BLOCK OF CODE"

## Slide 45: Using Subtraction To Set Flags
if(R2 > R1) {R2 <- R2 + R1}
Subtract R2 from R1. (R1 – R2)
What is the result if R2 < R1? N, Z, or P?
What is the result if R2 = R1? N, Z, or P
What is the result if R2 > R1? N, Z, or P?
If R2 < R1 (P) or R2 = R1 (Z) skip the add code.
  NOT R3, R2 (Invert R2 and put in R3)
  ADD R3, R3, #1 (Add 1 to R3, R3 is now –R2)
  ADD R3, R1, R3 (Add R3 to R1. Same as R1 – R2)
  BR_ _ _ #____ (Jump over add if R2 <= R1)
  ADD R2, R2, R1

## Slide 46: Results
if(R2 > R1) {R2 <- R2 + R1}
Subtract R2 from R1. (R1 – R2)
What is the result if R2 < R1? N, Z, or P?
What is the result if R2 = R1? N, Z, or P
What is the result if R2 > R1? N, Z, or P?
If R2 < R1 (P) or R2 = R1 (Z)skip the add.
  NOT R3, R2 (Invert R2 and put in R3)
  ADD R3, R3, #1 (Add 1 to R3, R3 is now –R2)
  ADD R3, R1, R3 (Add R3 to R1. Same as R1 – R2)
  BRPZ #1 (Jump over add if R2 > R1)
  ADD R2, R2, R1

## Slide 47: If - Else
IF CONDITION FALSE BRANCH TO BLOCK 2
BLOCK1
UNCONDITIONAL BRANCH (BRNZP or BR) OVER BLOCK2 SINCE BLOCK 1 WAS RUN
BLOCK2
if (R1 > R2)
{
R1 = R1 – R2 //Block 1
}
else
{
R1 = R2 – R1 //Block 2
}

## Slide 48: If - Else
IF CONDITION FALSE BRANCH TO BLOCK 2
BLOCK1
UNCONDITIONAL BRANCH OVER BLOCK2 SINCE BLOCK 1 WAS RUN
BLOCK2
if (R1 > R2)
{
R1 = R1 – R2 //Block 1
}
else
{
R1 = R2 – R1 //Block 2
}
BLOCK 1 (R1 <- R1 – R2)
NOT R2, R2 ADD R2, R2, #1 ADD R1, R2, R1
BLOCK 2(R1 <- R2 – R1)
NOT R1, R1 ADD R1, R1, #1 ADD R1, R2, R1

## Slide 49: If - Else
IF CONDITION FALSE BRANCH TO BLOCK 2
BLOCK1
UNCONDITIONAL BRANCH OVER BLOCK2 SINCE BLOCK 1 WAS RUN
BLOCK2
High Level Language (Java or C) |  | Assembly
if (R1 > R2) { R1 = R1 – R2 //Block 1 } else { R1 = R2 – R1 //Block 2 } | If R1 < R2 or R1 = R2 skip to BLOCK2 | NOT R3, R2 ADD R3, R3, #1 ADD R3, R1, R3 BRNZ #4
 | BLOCK1 | NOT R2, R2 ADD R2, R2, #1 ADD R1, R2, R1
 | skip BLOCK2 | BRNZP #3
 | BLOCK2 | NOT R1, R1 ADD R1, R1, #1 ADD R1, R2, R1

## Slide 50: Homework 3 & 4
USE THE DOCUMENTS ON ASULEARN FOR DETAILS ABOUT THESE ASSIGNEMNTS
Homework 3
  Print big then small
  Get two characters from the user using GETC
  Print the biggest character then the smallest character in that order as determined by their ASCII codes
Homework 4
  Print N digits
  Print 0 through some specified value

## Slide 51: Jumping Around
JSR – Jump to Subroutine or Jump Save Return.
  Return address (PC) saved in R7.
  11-Bit PC relative addressing.
JSRR – Jump to Subroutine
  Base register addressing.
JMP – Jump without saving return.
  Base register addressing.
RET – Special form of JMP
  Base register is always register R7.
BRNZP – Unconditional branch
  9-Bit PC relative addressing.

## Slide 52: TRAP
GETC - Get a character from keyboard (TRAP x20).
  No prompt is printed.
  Execution stops and waits for a key to be pressed.
  Store the ASCII code in R0.
OUT - Send a single character to output (TRAPx21).
  ASCII character must be stored in R0.
PUTS - Print null terminated string to the output (TRAP x22).
  ADDRESS of string must be stored in R0.
IN - Get character from keyboard (TRAP x23)
  Print prompt "Input a character>"
  Stop and wait for a key to be pressed
  Store the ASCII code in R0.
  Prints the character to the display.
PUTSP – Print null terminated string to the output (TRAP x24)
  Same as PUTS but assumes two characters per word.
  Address of string must be stored in R0.
HALT – Stop execution of the processor (TRAP x25).

## Slide 53: Printing Hello
HEX File | Assembly | 
3000 |  | ;Where the program starts
E002 | LEA R0, #2 | ;R0 <- Address of string
F022 | PUTS | ;DISPLAY <- String starting at R0
F025 | HALT | ;Stop the program
0048 | H | ;The string one character at a time
0065 | e | 
006C | l | 
006C | l | 
006F | o | 
0000 | /0 | ;NULL termination