## Slide 1: Number Systems

## Slide 2: Bits and Bytes
Computers use 1s and 0s in a form called binary
10010011 <- binary number
Each digit is a Binary digIT or BIT
1s and 0s are represented by voltage levels
Typically: 1 is 5v, 0 = 0v
Zero is NOT an absence of voltage it is a connection to the circuit ground.
Different voltage levels can be used (3v, 12v, …)
There are ranges to voltage levels
  0 = 0v to .5v 1 = 4.5v to 5.5v

## Slide 3: Number Representations
Decimal – normal base 10
Binary – unsigned base 2
2's Complement – signed base 2
Hexadecimal – base 16
ASCII (UNICODE) – text
Floating point – fractions or numbers with decimal points

## Slide 4: Binary
Convert decimal to binary.
  Small numbers convert to groups of powers of 2
    55 = 32 + 16 + 4 + 2 + 1
  Large numbers repeatedly divide by 2 and note remainder.
    1134
32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 1 | 1 | 1

## Slide 5: Convert decimal to binary
Large numbers repeatedly divide by 2 and note remainder.
    1134 / 2 = 567 r 0
    567 / 2 = 283 r 1
    283 / 2 = 141 r 1
    141 / 2 = 70 r 1
    70 / 2 = 35 r 0
    35 / 2 = 17 r 1
    17 / 2 = 8 r 1
    8 / 2 = 4 r 0
    4 / 2 = 2 r 0
    2 / 2 = 1 r 0
    1 / 2 = 0 r 1 <- keep going until answer is zero
    Answer is remainders starting at bottom: 10001101110

## Slide 6: Binary to Decimal
Add up the column values
  10010110
  128 + 16 + 4 + 2 = 150
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0

## Slide 7: Representing Negative Numbers
Signed Magnitude
  Set sign bit for negative values
  Easiest for humans, not so easy for computer
One's Complement
  Invert all bits for negative values
Two's Complement
  Invert all bits and add 1 for negative values
  Easiest for computers, not so easy for humans
  Most commonly used

## Slide 8: Signed Magnitude
Use the leading bit to indicate the sign
  0 means positive
  1 means negative
We need to know how many bits
Represent -15 as 6 bit signed magnitude
  15 = 8 + 4 + 2 + 1 = 1111 (convert as unsigned)
  001111 (write as six bits)
  101111 (1 in first position means negative)

## Slide 9: 2's Complement
Allows both positive and negative numbers
Works because of a fixed number of bits
Assume you have only 5 bits to work with
You can store 00000 to 11111
Adding a number to its additive identity should give zero so 7 + (-7) = 0
00111 (7)
+11001 (?)
00000 (0)
11001 must be -7

## Slide 10: Decimal to 2's Complement
If the number is positive
  Treat as unsigned binary
If the number is negative
  Convert as unsigned
  Invert all bits and add 1
Convert 17 and -23 to 6 bit 2's complement

## Slide 11: Decimal to 2's Complement Example
Convert 17 and -23 to 6 bit 2's complement
  17 (Positive so treat as unsigned binary and done)
  17 = 16 + 1 = 010001 (make sure to write the number as six bits)
  Answer: 010001
  -23 (negative so convert as unsigned then do the following)
  23 = 16 + 4 + 2 + 1 = 010111 (six bits is important)
  101000 (invert all bits)
  101001 (add 1)
  Answer: 101001 (How can you verify this is -23?)

## Slide 12: 5 Bit Comparison
Number | Signed Magnitude | 1's Complement | 2's Complement
0 | 00000 or 10000 | 00000 or 11111 | 00000
1 | 00001 | 00001 | 00001
2 | 00010 | 00010 | 00010
3 | 00011 | 00011 | 00011
5 | 00101 | 00101 | 00101
15 | 01111 | 01111 | 01111
-1 | 10001 | 11110 | 11111
-2 | 10010 | 11101 | 11110
-5 | 10101 | 11010 | 11011
-11 | 11011 | 10100 | 10101
-15 | 11111 | 10000 | 10001
-16 | - | - | 10000
See Figure 2.1 in book |  |  | 

## Slide 13: 2's Complement Notes
Binary | Unsigned | 2's Complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
Positive numbers are exactly the same
Half as many non-negative integers as unsigned
-1 is always all 1s no matter how many bits
(111111 = -1 with six bits)
The most negative number is always leading 1 followed by zeros
(100000 is -32 with six bits)
There are the same number of negative and non-negative values
The range is (+2k-1-1) to (-2k-1)
What is the range for 8 bits?

## Slide 14: 2's Complement Shortcut
Invert all bits and add 1
The following number does something special
10100000 Decimal
01011111 Invert all bits.
01100000 Add 1
When we invert and add 1 we get the same pattern in the red bits above as we started with.
Shortcut – Keep zero bits from right to left up to, and including the first 1. Invert everything else.
Note that you don’t add 1 if you use this shortcut.

## Slide 15: 2s Complement Shortcut Practice
Convert these to decimal using the shortcut
10100000
10001100
00110000
11111101

## Slide 16: 2s Complement Shortcut Practice
Convert these to decimal using the shortcut
10100000 = 01100000 = -96
10001100 = 01110100 = -116
00110000 = 00110000 = +48 (Positive)
11111101 = 00000011 = -3
Bold, Black bits are kept : Red, italic bits are inverted.

## Slide 17: Biggest and smallest number
What is the biggest number you can store using unsigned binary and 12 bits?
  2n-1 (where n = number of bits)
What is the biggest number you can store using 2's complement binary and 12 bits? Why n-1 below?
  2(n-1)-1 (where n = number of bits)
What is the smallest number you can store using unsigned binary and 12 bits?
  Always 0
What is the smallest number you can store using 2's complement binary and 12 bits?
  -2(n-1) (where n = number of bits)

## Slide 18: Biggest and smallest number
What is the biggest number you can store using unsigned binary and 12 bits?
212-1 = 4095
What is the biggest number you can store using 2's complement binary and 12 bits?
2(12-1)-1 = 2(11)-1 = 2047
What is the smallest number you can store using unsigned binary and 12 bits? Smallest will always be zero.
0
What is the smallest number you can store using 2's complement binary and 12 bits? Smallest is -2n.
-2(12-1) = -2(11) = -2048

## Slide 19: How many bits to represent a number?
How many bits do you need to represent +111 in unsigned numbers?
How many bits do you need to represent -111 in unsigned numbers?
How many bits do you need to represent +111 in 2's complement numbers?
How many bits do you need to represent -111 in 2's complement numbers?

## Slide 20: How many bits to represent a number?
How many bits do you need to represent +111 in unsigned numbers?
  Next higher power of 2 = 128 = 27 = 7
How many bits do you need to represent -111 in unsigned numbers?
You cant.
How many bits do you need to represent +111 in 2's complement numbers?
  Next higher power of 2 = 128 = 27 = 2's comp always needs 1 more = 8
How many bits do you need to represent -111 in 2's complement numbers?
  Next higher power of 2 = 128 = 27 = 2's comp always needs 1 more = 8
  It doesn’t matter if the number you want to represent is + or - , 2's comp always needs one more.

## Slide 21: Using Metric Prefixes
Power | Value | Prefix name | Approximate Decimal value
210 | 1K | Kilo | ~1,000 (~ a thousand)
220 | 1M | Mega | ~1,000,000 (~a million
230 | 1G | Giga | ~1,000,000,000 (~a billion)
240 | 1T | Tera | ~1,000,000,000,000 (~a trillion)
250 | 1P | Peta | ~1,000,000,000,000,000 (~ a quadrillion)
260 | 1E | Exa | ~1,000,000,000,000,000,000 (~a quintillion?)
How many bits would you need to store 50,000,000,000 using unsigned numbers?
The exponent on the next higher power of two is?

## Slide 22: Using Metric Prefixes
Power | Value | Prefix name | Approximate Decimal value
210 | 1K | Kilo | ~1,000 (~ a thousand)
220 | 1M | Mega | ~1,000,000 (~a million
230 | 1G | Giga | ~1,000,000,000 (~a billion)
240 | 1T | Tera | ~1,000,000,000,000 (~a trillion)
250 | 1P | Peta | ~1,000,000,000,000,000 (~ a quadrillion)
260 | 1E | Exa | ~1,000,000,000,000,000,000 (~a quintillion?)
How many bits would you need to store 50,000,000,000 using unsigned numbers?
The exponent on the next higher power of two is? 64G
What is the exponent?

## Slide 23: Using Metric Prefixes
Power | Value | Prefix name | Approximate Decimal value
210 | 1K | Kilo | ~1,000 (~ a thousand)
220 | 1M | Mega | ~1,000,000 (~a million
230 | 1G | Giga | ~1,000,000,000 (~a billion)
240 | 1T | Tera | ~1,000,000,000,000 (~a trillion)
250 | 1P | Peta | ~1,000,000,000,000,000 (~ a quadrillion)
260 | 1E | Exa | ~1,000,000,000,000,000,000 (~a quintillion?)
How many bits would you need to store 50,000,000,000 using unsigned numbers?
The exponent on the next higher power of two is? 64G
What is the exponent? 64 * 1G = 26 * 230= 236 = 36 bits
What about in 2's complement?

## Slide 24: Sign extension +
+5 in 4-bit 2's complement is
0101
+5 in 8 bit 2's complement is
00000101
+5 in 16 bit 2's complement is 0000000000000101
What about 32Bit 2's complement?

## Slide 25: Sign extension -
-5 in 4-bit 2's complement is
1011
-5 in 8 bit 2's complement is
11111011
-5 in 16 bit 2's complement is
1111111111111011
What about 32Bit 2's complement?

## Slide 26: Sign Extension
When expanding a signed value into a larger storage size, the sign must be extended.
Whatever the old sign bit was must fill all of the new empty bits in the bigger number
Expand 4 bits to 8 |  |  |  | 1 | 0 | 0 | 1
Fill sign bits here |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1

## Slide 27: Sign Extension
When expanding a signed value into a larger storage size, the sign must be extended.
Whatever the old sign bit was must fill all of the new empty bits in the bigger number
Expand 4 bits to 8 |  |  |  | 0 | 1 | 0 | 1
Fill sign bits here |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1

## Slide 28: Zero Extension
Zero extension is placing zeros in the new expanded bits regardless of sign.
Unsigned numbers are always zero extended.
Expand 4 bits to 8 |  |  |  | 1 | 1 | 0 | 1
Zero fill here |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 1 | 0 | 1

## Slide 29: Unsigned Overflow
Adding 4 bit unsigned numbers
Can't store carry out-> | 0 | 1 | 0 | 0 |  | <-Carry
 |  | 0 | 1 | 0 | 1 | (5)
+ |  | 0 | 1 | 1 | 0 | (6)
 |  | 1 | 0 | 1 | 1 | (11)
Can't store carry out-> | 1 | 1 | 0 | 0 |  | <-Carry
 |  | 1 | 1 | 0 | 0 | (12)
+ |  | 0 | 1 | 1 | 1 | (7)
 |  | 0 | 0 | 1 | 1 | ()

## Slide 30: Signed Overflow Positive
Adding 4 bit signed numbers
Can't store carry out-> | 0 | 0 | 0 | 0 |  | <-Carry
 |  | 0 | 0 | 1 | 1 | (3)
+ |  | 0 | 1 | 0 | 0 | (4)
 |  | 0 | 1 | 1 | 1 | (7)
Can't store carry out-> | 0 | 1 | 0 | 0 |  | <-Carry
 |  | 0 | 1 | 0 | 1 | (5)
+ |  | 0 | 1 | 1 | 0 | (6)
 |  | 1 | 0 | 1 | 1 | (-5)

## Slide 31: Signed Overflow Negative
Adding 4 bit signed numbers
Can't store carry out-> | 1 | 1 | 0 | 0 |  | <-Carry
 |  | 1 | 1 | 0 | 1 | (-3)
+ |  | 1 | 1 | 1 | 0 | (-2)
 |  | 1 | 0 | 1 | 1 | (-5)
Can't store carry out-> | 1 | 0 | 1 | 0 |  | <-Carry
 |  | 1 | 0 | 1 | 1 | (-5)
+ |  | 1 | 0 | 1 | 0 | (-6)
 |  | 0 | 1 | 0 | 1 | (+5)

## Slide 32: Signed Overflow Negative
Many processors don't have a subtraction operation. They simply add a negative.
Subtracting -2 is the same as adding +2.
 | 1 | 0 | 0 |  | <-Carry
 | 0 | 1 | 0 | 1 | (5)
- | 0 | 0 | 1 | 1 | (3) (subtracting 3 is same as adding -3)
 | ? | ? | ? | ? | (2)
 | 1 | 0 | 1 |  | <-Carry
 | 0 | 1 | 0 | 1 | (5)
+ | 1 | 1 | 0 | 1 | (-3) (subtracting 3 is same as adding -3)
 | 0 | 0 | 1 | 0 | (2)

## Slide 33: Signed Overflow Negative
Many processors don't have a subtraction operation. They simply add a negative.
Determine overflow by converting subtraction to addition.
 | 1 | 0 | 0 |  | <-Carry
 | 1 | 0 | 1 | 1 | (-5)
- | 0 | 1 | 0 | 0 | (4) (subtracting 4 is same as adding -4)
 | ? | ? | ? | / | (2)
 | 0 | 0 | 0 |  | <-Carry
 | 1 | 0 | 1 | 1 | (-5)
+ | 1 | 1 | 0 | 0 | (-4) (subtracting 3 is same as adding -3)
 | 0 | 1 | 1 | 1 | Negative + Negative = Positive = Overflow

## Slide 34: Detecting overflow
Unsigned: A carry out of 1 is always an overflow.
Signed – Computer: If the carry in and the carry out of the most significant bit are different, overflow has occurred.
Signed – Human: If you add two positive numbers and get a negative result or you add two negative numbers and you get a positive result, overflow has occurred.
Note: You can never have overflow when adding a negative and a positive number.

## Slide 35: Bit Twiddling
Sometimes you want to set specific bits inside of a binary number.
Sometimes you want to examine specific bits inside of a binary number.
Bitwise operators allow manipulation and examination of specific bits.
Operators are: and, or, xor, not, shift left, shift right.

## Slide 36: Operators
Operator | Symbol | Example
And | & | And each bit: 1010 & 1100 = 1000
Or | ¦ | Or each bit: 1010 ¦ 1100 = 1110
Xor | ^ | Xor each bit: 1011 ^ 1001 = 0010
Right Shift (Sign Extends for signed numbers. Zero extends unsigned numbers) | >> | Shift all bits to the right a given number of bits 0100 >> 1 = 0010 0100 >> 2 = 0001 0110 >> 2 = 0001 (bits fall off end) 1100 >> 2 = 1111 (signed numbers) 1100 >> 2 = 0011 (unsigned numbers)
Left Shift | << | Shift all bits to the left a given number of bits 0011 << 1 = 0110 0011 << 2 = 1100 1011 << 2 = 1100 (bits fall off end)
Not | ~ | Invert all bits ~1010 = 0101

## Slide 37: Truth Tables
A | B | AND
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | OR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | NOT
0 | 1
1 | 0

## Slide 38: Clearing bits with AND
0110100101001000
Set the red bits to all zeros.
Boolean laws
x & 0 = 0
x & 1 = x
0110100101001000
& 1111111000011111
0110100000001000
A | B | AND
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 39: Clearing Bits Practice
Show how to clear the red bits.
0110100101011000
0110100101011000
0110100101011000
A | B | AND
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 40: Masking
Sometimes you want to just look at a subset of bits.
A MASK allows filtering out unwanted bits.
If I want to look only at the bits in red I can create a mask and use the AND operation
0110100101011000(Number)
&0000000111100000(Mask)
0000000101000000(Result)

## Slide 41: Setting bits with OR
0110100101001000
Set the red bits to all ones.
Boolean laws
x | 0 = x
x | 1 = 1
0110100101011000
| 0000000111100000
0110100111111000
A | B | OR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 42: Setting Bits Practice
Show how to set the red bits.
0110100101011000
0110100101011000
0110100101011000
A | B | OR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 43: Bit Vector Example
Each bit represents the presence or absence of an item.
A = { b, d, m, z}
Represent A as a bit vector where the domain is all letters.
Assume each letter is positional a=1, b=2, c=3, etc.
How many bits will we need?
How many bytes?
What data type to use in Java?

## Slide 44: Bit Vector Solution
Each bit represents the presence or absence of an item.
A = { b, d, m, z}
Represent A as a bit vector where the domain is all letters.
Assume each letter is positional a=1, b=2, c=3, etc.
How many bits will we need? 26
How many bytes? 4
What data type to use in Java? int
abcdefghijklmnopqrstuvwxyz------
01010000000010000000000001000000

## Slide 45: Bit Vector Practice
Assuming the letters bit vector what set would the following represent?
A=11010001000000000000000000000000
B=10000101001000000000000000000000
How could we calculate C if C= A  B
How could we remove element a from B?
How could we add y and z to B?

## Slide 46: Clearing all bits with XOR
What is the result?
00010010000100010011100010100100
^00010010000100010011100010100100
int a = 25;
a = a ^ a;
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 47: Checking equality with XOR
What is the result?
a = 00000000000000000000000000000100
b = 00000000000000000000000000000111
a ^ b = ?
lda a
xor b
bz addr
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 48: Sign Extension Example
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0
This is an example of an LC3 instruction.
Bits 0 through 8 represent a 2's complement number.
What is that 2's complement number?

## Slide 49: Sign Extension Example
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0
The number is -12.
Which of these will give the correct value?
offset_value = instruction & 0x01FF
offset_value = instruction | 0xFE00

## Slide 50: Sign Extension Example
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
The number is +12.
Which of these will give the correct value?
offset_value = instruction & 0x01FF
offset_value = instruction | 0xFE00

## Slide 51: Sign Extension Example
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | DR or SR |  |  | 2's comp value added to PC |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
The number is +12.
To be able to sign extend you must check the high order bit.
if (instruction & 0x0100 == 0)
offset_value = instruction & 0x01FF
else
offset_value = instruction | 0xFE00

## Slide 52: Octal – Base 8
Convert decimal to octal
  Repeatedly divide by 8.
Convert octal to decimal
  Sum of column digits x column values.
Convert octal to binary
  Write each digit as 3 bit binary
Convert binary to octal
  Convert each group of three bits, starting from least significant, to a single octal digit.

## Slide 53: Hexadecimal – base 16
Sometimes called simply Hex
Convert decimal to hexadecimal
  Repeatedly divide by 16.
Convert hexadecimal to decimal
  Sum of column digits x column values.
Convert hexadecimal to binary
  Write each digit as 4 bit binary
Convert binary to hexadecimal
  Convert each group of four bits, starting from least significant, to a single hex digit.

## Slide 54: Convert the following
45610 to octal.
2748 to decimal.
101010001010 to octal.
2748 to binary.
512610 to hexadecimal.
AB416 to decimal.
101010001010 to hexadecimal.
AB416 to binary.

## Slide 55: Using Hexadecimal
In many programming languages, hex values are preceded by 0x
  0x123 or 0X123
Your book simply uses an x
  x123 or X123
Hexadecimal is a convenient way of representing binary information, not just binary numbers.
For example, the following binary could represent pixel data, part of an integer, a 16 bit floating point number, or the word Hi in ascii.
0100100001101001
Regardless of its meaning, the value can still be stored for convenience as hexadecimal as the value
x4869

## Slide 56: Binary Fractions
What does .3 mean in a number like 1.3?
Why?

## Slide 57: Binary Fractions
What does .3 mean in a number like 1.3?
It means 3/10
So what would 11.11 mean in binary?
100s | 10s | 1s | . | 1/10 | 1/100 | 1/1000
 |  | 1 | . | 3 |  | 

## Slide 58: Binary Fractions
What does 11.11 mean in binary?
It means 2 + 1 + ½ + ¼ = 3¾ or 3.75
4s | 2s | 1s | . | 1/2 | 1/4 | 1/8
 | 1 | 1 | . | 1 | 1 | 

## Slide 59: Fractional Binary to Decimal
The same as non-fractional numbers.
Add up the column values where a 1 is the digit.
Convert 1011.1101
8 + 2 + 1 + ½ + ¼ + 1/16 = 11 & 13/16

## Slide 60: Fractional Binary to Decimal (Easy)
Whole part same as non-fractional numbers.
Numerator for fraction will be the binary number to the right of radix.
Denominator for fraction will be the least column value.
Convert 1011.1101 = Decimal part is 13
Convert 1011.1101 = column value is 1/16
Answer is 11 & 13/16

## Slide 61: Decimal to Fractional Binary
Convert whole part as learned earlier.
  That is repeatedly divide by 2.
Convert fractional part by repeatedly multiplying by 2.
Convert 12.3 to fractional binary | 
Convert whole part (12) | Convert fraction (0.3)
12 / 2 = 6r0 | 0.3 * 2 = 0.6
6 / 2 = 3r0 | 0.6 * 2 = 1.2
3 / 2 = 1r1 | 0.2 * 2 = 0.4
1 / 2 = 0r1 | 0.4 * 2 = 0.8
1100 (reverse order) | 0.8 * 2 = 1.6
 | 0.6 * 2 = 1.2
 | 0.2 * 2 = 0.4
 | … When do we quit?

## Slide 62: Decimal to Fractional Binary
Done with the fractional part when:
  Result becomes zero
  Result repeats
  We have expressed a given number of bits
Which should we use for the example to the right?
1100.01001
Convert 12.3 to fractional binary | 
Convert whole part (12) | Convert fraction (0.3)
12 / 2 = 6r0 | 0.3 * 2 = 0.6
6 / 2 = 3r0 | 0.6 * 2 = 1.2
3 / 2 = 1r1 | 0.2 * 2 = 0.4
1 / 2 = 0r1 | 0.4 * 2 = 0.8
1100 (reverse order) | 0.8 * 2 = 1.6
 | 0.6 * 2 = 1.2
 | 0.2 * 2 = 0.4
 | .0100110… (in order)
 | … When do we quit?

## Slide 63: IEEE Floating Point Storage
Floating point numbers are stored as binary, normalized scientific notation.
Store Sign, Exponent and Mantissa in a single unit.
We will learn 16 and 32 bit floating point numbers.
Size | Sign bits | Exponent Bits | Mantissa bits
16 | 1 | 5 | 10
32 | 1 | 8 | 23
64 | 1 | 11 | 51
128 | 1 | 16 | 113

## Slide 64: Scientific notation
Decimal
1.234 x 102
Binary
1.10101 x 23
The red above is the mantissa.
The green above is the exponent.
Normalized – Only one non-zero digit to the left of the radix.

## Slide 65: Writing Normalized SN
Normalize the following.
111.11101
0.0000110
1001.111 x 22
0.0111 x 2-4

## Slide 66: Writing Normalized SN Answers
Normalize the following.
111.11101 = 1.1111101 x 22
0.0000110 = 1.10 x 2-5
1001.111 x 22 = 1.001111 x 25
0.0111 x 2-4 = 1.11 x 2-6

## Slide 67: IEEE 16 Bit Floating Point
Sign 1 bit
  0 for positive, 1 for negative
Exponent 5 bits
  Stored as Excess-15
Mantissa 10 bits
  Normalized – Remove leading 1
S | E | E | E | E | E | M | M | M | M | M | M | M | M | M | M
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 68: Excess-15
Add excess before storing.
  When converting and storing in IEEE form.
  The exponent + excess is known as the Characteristic
  You store the characteristic.
Subtract 15 after removing.
  When removing from and interpreting IEEE form.
  The exponent is the characteristic – 15.

## Slide 69: Convert to Floating Point
Write your number in normalized binary scientific notation if not already done for you. The mantissa of this number MUST have enough bits to fill the mantissa portion of the floating point number. (10 or 24)
Calculate the characteristic by adding the excess to the exponent.
Store the sign: 0 = Positive, 1 = Negative
Store the characteristic as calculated above.
Remove the leading 1 from the mantissa and store.
For most quizzes and homework write the value as a hexadecimal value.

## Slide 70: 16 Bit Example
Store 1.11100 x 24 int 16 bit IEEE form.
  What is the sign?
  What is the exponent?
  What is the mantissa?

## Slide 71: Convert to Floating Point
Write your number in normalized binary scientific notation if not already done for you. The mantissa of this number MUST have enough bits to fill the mantissa portion of the floating point number.
+1.11100 x 24
Calculate the characteristic by adding the excess to the exponent.
Characteristic = exponent + excess = 4 + 15 = 19
Store the sign: 0 = Positive, 1 = Negative
0
Convert the characteristic to binary and store.
010011
Remove the leading 1 from the mantissa and store. Make sure the entire area for mantissa bits is filled.
0100111110000000
For most quizzes and homework write the value as a hexadecimal value.
0100 1111 1000 0000 = 0x4F80

## Slide 72: Convert to decimal from Floating Point
If the number is in hexadecimal, convert to a binary pattern.
Calculate the characteristic by converting the exponent bits to decimal.
Calculate the exponent by subtracting the excess from the characteristic.
Write the mantissa bits and add 1. to the beginning.
Write x 2exponent using the exponent calculated above.
Put in the sign as determined by bit 1.
Convert from SN to normal fractional binary by moving the radix the required number of bits in the specified direction.
Convert the fractional binary to decimal as described previously.

## Slide 73: 16 Bit Example
Convert 0xC640 from 16 bit IEEE to decimal
  What is the sign?
  What is the exponent?
  What is the mantissa?

## Slide 74: Convert to decimal from Floating Point
0xC640
If the number is in hexadecimal, convert to a binary pattern.
1100011001000000
Calculate the characteristic by converting the exponent bits to decimal.
10001 = 17
Calculate the exponent by subtracting the excess from the characteristic.
17 – 15 = 2
Write the mantissa bits and add 1. to the beginning.
1.1001
Write x 2exponent using the exponent calculated above.
1.1001 x 22
Put in the sign according to bit 1.
Convert from SN to normal fractional binary by moving the radix the required number of bits in the specified direction.
Convert the fractional binary to decimal as described previously.

## Slide 75: IEEE 32 Bit Floating Point
Sign 1 bit
  0 for positive, 1 for negative
Exponent 8 bits
  Stored as Excess-___?
Mantissa 23 bits
  Normalized – Remove leading 1
S | E | E | E | E | E | E | E | E | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M | M
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 76: Excess-127
Add excess (127) before storing.
  When converting and storing in IEEE form.
  The exponent + excess is known as the Characteristic
  You store the characteristic.
Subtract excess (127) after removing.
  When removing from and interpreting IEEE form.
  The exponent is the characteristic – 127.

## Slide 77: Floating point conversions 16 Bit
Convert from decimal to 16 bit floating point:
10.09375
2.71
Convert from 16 bit floating point:
xCB40
x5112

## Slide 78: Floating point conversion 32 bit
Convert from decimal to 32 bit floating point:
10.09375
2.71
Convert from 32 bit floating point:
C18C0000
BF980000

## Slide 79: Special Numbers
IEEE Defines certain special numbers
  Zero (+ and -)
  Denormalized
  Infinity (+ and -)
  Not a Number (NaN)
Special numbers use patterns of zeros in the characteristic and mantissa field
For normal floating point representation
  You cannot use all zeros in the characteristic.
  You cannot use all zeros in the mantissa
For this course the only special number you need to know is how to store zero.

## Slide 80: Zero and Denormalized
Zero
  We cannot represent zero in the normal floating point representation due to the assumption of a leading 1.
  Zero is a special value denoted with all zeros in the characteristic and all zeros in the mantissa.
  Note that -0 and +0 are distinct values, though they both compare as equal.
  +0 = 0x00000000 -0 = 0x80000000 (32 bit)
  +0 = 0x0000 -0 = 0x8000 (16 bit)
Denormalized
  Denormalized means the scientific notation has a zero to the left of the radix instead of a 1.
  0.1 x 23 instead of 1.0 x 22
  Denormalized is represented as all zeros in the characteristic and anything except zero in the manitssa.
  From this you can interpret zero as a special type of denormalized number.

## Slide 81: Infinity
Infinity
  The values +infinity and -infinity are denoted with all ones in the characteristic and all zeros in the mantissa.
  The sign bit distinguishes between negative infinity and positive infinity.
  Being able to denote infinity as a specific value is useful because it allows operations to continue past overflow situations. Operations with infinite values are well defined in IEEE floating point.
  Hex values
  +∞ = 0x7C00 -∞ = 0xFC00 (16 bit)
  +∞ = 0x7F800000 -∞ = 0xFF800000 (32 bit)

## Slide 82: Not A Number
Not A Number (Nan) is used to represent a value that does not represent a real number.
NaN's are represented by a bit pattern with a characteristic of all ones and a non-zero mantissa.
There are two categories of NaN: QNaN (Quiet NaN) and SNaN (Signalling NaN).
  A QNaN is a NaN with the most significant fraction bit set. QNaN's propagate freely through most arithmetic operations. These values pop out of an operation when the result is not mathematically defined.
  An SNaN is a NaN with the most significant fraction bit clear. It is used to signal an exception when used in operations. SNaN's can be handy to assign to uninitialized variables to trap premature usage.
Semantically, QNaN's denote indeterminate operations, while SNaN's denote invalid operations.

## Slide 83
Sign | Exponent (e) | Fraction (f) | Value
0 | 00⋯00 | 00⋯00 | +0
0 | 00⋯00 | 00⋯01 ⋮ 11⋯11 | Positive Denormalized Real 0.f × 2(-b+1)
0 | 00⋯01 ⋮ 11⋯10 | XX⋯XX | Positive Normalized Real 1.f × 2(e-b)
0 | 11⋯11 | 00⋯00 | +Infinity
0 | 11⋯11 | 00⋯01 ⋮ 01⋯11 | SNaN
0 | 11⋯11 | 10⋯00 ⋮ 11⋯11 | QNaN
1 | 00⋯00 | 00⋯00 | -0
1 | 00⋯00 | 00⋯01 ⋮ 11⋯11 | Negative Denormalized Real -0.f × 2(-b+1)
1 | 00⋯01 ⋮ 11⋯10 | XX⋯XX | Negative Normalized Real -1.f × 2(e-b)
1 | 11⋯11 | 00⋯00 | -Infinity
1 | 11⋯11 | 00⋯01 ⋮ 01⋯11 | SNaN
1 | 11⋯11 | 10⋯00 ⋮ 11.11 | QNaN

## Slide 84: Operations and Results
Operation | Result
n ÷ ±Infinity | 0
±Infinity × ±Infinity | ±Infinity
±nonzero ÷ 0 | ±Infinity
Infinity + Infinity | Infinity
±0 ÷ ±0 | NaN
Infinity - Infinity | NaN
±Infinity ÷ ±Infinity | NaN
±Infinity × 0 | NaN